## Slide 1
LECTURE – RADIACTIVE ENERGY TRANSFER
RADIATION (Chapter 8)
Explain characteristics of electromagnetic radiation – Emitted and received by a surface
Calculate the magnitude and spectra quality of electromagnetic radiation
Explain energy emitted by an ideal body (black body) and real (gray) bodies. Definition of emissivity

## Slide 2
Length or time
wavelength
frequency
Speed of the light

## Slide 3
Thermal Radiation = 10-7m – 10-4m
0.1μm - 100 μm

## Slide 4
Facts about Radiant Heat Transfer
Conduction: Heat is transferred from one part of the body
to another
Convection: Heat is transferred by the actual mixing of the material and by conduction
Radiation: Heat is transferred by electromagnetic radiation. It may transfer through the space or vacuum. The media
through which the heat (by radiation) is transferred usually is not heated

## Slide 5
Heat Radiation Mechanism
1. The thermal energy of a hot source, e.g. wall of a furnace at T1, is converted into energy in the form of electromagnetic wave
These waves travel through the intervening space in straight lines and strike a cold object at T2, such as for example a furnace tube containing water to be heated
Some of the energy of those electromagnetic waves that strike the body are absorbed by the body and converted back to thermal energy (heat)
T1
T2
T1
T1
Furnace

## Slide 6
What happens with the radiation once reaches
an object ?
Absorbed
Reflected
Incident
Transmitted
Reflectivity
Absorptivity
Transmissivity
Specular Reflection: Angle
of incidence is equal to angle
of reflection
Diffuse Reflection: Waves
are reflected in all directions

## Slide 7
Reflectivity
Absorptivity
Transmissivity
Wavelength ( )
0.4
0.5
0.6
0.7
1.0
2.0
10.0
Fraction
0.2
0.4
0.6
0.8
1.0
Absorbed
Reflected
Transmitted
Spectral Values in Biological materials
Shadow region of the plant, where there is no major production
of chlorophyll due to little absorption

## Slide 8
Absorption and Transmission in Biomaterials
x
F
Fo
F: Flux W/m2
Type of Electromagnetic Wave | Frequency in MHz | Wavelength in air (cm) | Penetration depth
Infrared Microwave Radio frequency | 70,000,000 2,450 27 | 0.0004 12 1100 | Few microns Few centimeters Hundred centimeters
Importance in
our daily life, and
In Thanksgiving!!

## Slide 9
Source | Exposure (U.S. Average)
External Background Radiation | 0.54 mSv/year
Natural K-40 and Other Radioactivity in Body | 0.29 mSv/year
Air Travel Round Trip (NY-LA) | 0.05 mSv/year
Chest X-Ray Effective Dose | 0.01 mSv/film
Radon in the Home | 2.28 mSv/year
Man-Made (medical x rays, etc.) | 3.14 mSv/year
RADIATION EXPOSURE OF VARIOUS SOURCES
mSv/y is defined as "the average” accumulated background radiation dose to an individual for 1 year
Note: Radiation limits: 1mSv/y for the general public, 20mSv/y for a registered radiation worker

## Slide 10
Thermal Radiation of an Ideal (Black) Body
T1
Energy between two wavelengths
Total Energy Emitted
Fraction of Total Energy Emitted
between two wavelengths

## Slide 11
Thermal Radiation of an Ideal (Black) Body
Black Body: It absorbs all energy, nothing is
reflected or transmitted (black body)
Concept of Black Body
Radiation Emitted from a Black Body (Plancks’ Law)
c: Light velocity 3x108 m/s
h: Planck’s constant 6.625x10-34 J . s
Boltzmann constant 1.380 x10-23J/K
T: Absolute temperature in K

## Slide 12
Thermal Radiation of an Ideal (Black) Body
Units

## Slide 13
Thermal Radiation of an Ideal (Black) Body
Planck’s Law
There is a relationship between the peak of emission and temperature
Emitted radiation varies continuously
with wavelength
At any wavelength the magnitude of radiation increases with temperature

## Slide 14
Thermal Radiation of an Ideal (Black) Body
Planck’s Law
Sun Temperature = 5,800K
Temperature = 800K
(visible light)
(infrared)

## Slide 15
Thermal Radiation of an Ideal (Black) Body
Planck’s Law
5.67x10-8 W/m2.K4
Stefan –Boltzmann constant
Stefan –Boltzmann’s Law
All Energy Emitted by a Black Body
Energy Emitted by a
Black Body at a given

## Slide 16
Fraction of Energy Emitted by a Black
Body between two wavelengths

## Slide 17
Fraction of Energy Emitted by a Black
Body between two wavelengths
By defining

## Slide 18
Fraction of Energy Emitted by a Black
Body between two wavelengths
0 | 0
200 | 7.010E-27
400 | 2.20179E-12
600 | 9.96926E-8
2000 | 0.0670396
Table 8.2

## Slide 19
Example: Calculate the fraction of Solar Energy
that is in the visible region 0.38μm-0.76μm
From Table 2 by interpolation
Fraction of Solar Energy in the visible region
= 0.5491-0.1013 = 0.4478 (44.8%)

## Slide 20
Thermal Radiation from a Real Body
T
Ideal Black Body
T
Real Body
Define Total Emissivity

## Slide 21
Typical Emissivities of Biomaterials
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1.0
water
Biomaterials
All paints
Aluminum Oxidized
Aluminum polished

## Slide 22
Concept of Gray Body
(ALSO AN IDEAL MATERIAL BUT THAT EMMITS/ABSORBS LESS ENERGY THAN THE BLACK BODY)
Wavelength (μm)
Monochromatic Emissivity
That the Monochromatic Emissivity is independent of the wavelength
What assumption is used to consider a Gray Body as an ideal material ?

## Slide 23
Emission from Human Bodies
Microwave Thermography for Clinical Uses
Infrared
Microwave (high penetration)
Research
on new
detectors
of low radiation
Intensity

## Slide 24
Absorbed
Reflected
Incident
Radiation
Transmitted
Specular Reflection: Angle
of incidence is equal to angle
of reflection
Diffuse Reflection: Waves
are reflected in all direcctions
Review
Reflectivity
Absorptivity
Transmissivity

## Slide 25
Review of Previous Concepts
Black Body
5.67x10-8 W/m2.K4
Real Body

## Slide 26
MORE RADIACTIVE ENERGY
TRANSFER RADIATION
Describe relationships between body Emissivity and its energy absorption. Kirchhoff’s Law.
Define and characterize View Factors
Application problems

## Slide 27
Kirchhoff’s Law
TS
Enclosure (Black Body)
Steady State Conditions
Energy Balance for Body 1

## Slide 28
Kirchhoff’s Law
Steady State Conditions
Energy Balance for Body 1
Energy Absorbed
by body A1
Energy Emitted
by body A1

## Slide 29
Kirchhoff’s Law
Steady State Conditions
Energy Balance for Body 1
Using the same balance for each body

## Slide 30
Kirchhoff’s Law
For an enclosure
We could gain much practical use if we could figure out
what’s required for

## Slide 31
The energy balance on a per unit wavelength basis, can be calculated as:
If we also have either el = al, or el and al are independent of l, then
Kirchhoff’s Law
Radiation between surfaces are greatly simplified
if the equation above may be applied

## Slide 32
For a gray surface, the spectral emissivity e and absorptivity a of a given surface are independent of wavelength for the spectral region corresponding to emitted and incident radiation
  Unless spectral regions of emission and irradiation are widely separated, the assumption of gray surface is widely used in practical applications
GRAY BODY/SURFACE

## Slide 33
Concept of View Factors

## Slide 34
Concept of View Factors

## Slide 35
CONCEPTS ON SURFACE EMISSION
Real Surface
Solid Angle
General case
Diffuse Emitter
Ideal
Black
Body
Emission of
Radiation
These angles characterize
the surface and its emission

## Slide 36
In general, we have:
For diffuse irradiation or for a diffuse surface, we have:
For irradiation from a black body or for a gray diffuse surface, we have:
Engineering Simplifications

## Slide 37
View Factors
T1
T2
A1
A2
Net heat flow is a function of the size, shape, and
orientation of the radiant surfaces

## Slide 38
View Factors – General Case
dA1
dA2
Energy emitted and reflected

## Slide 39
View Factors – General Case
Way to calculate them

## Slide 40
View Factors – General Case
Let’s assume that bodies 1 and 2 are black bodies
Net Heat Flow

## Slide 41
View Factors – General Case
Net Heat Flow

## Slide 42
View Factors
Infinite Parallel Black Planes

## Slide 43
View Factors
Infinite Parallel Gray Planes (there is reflection
of energy)
Energy Emitted from Surface 1 to surface 2
Energy Absorbed by surface 2
Energy Reflected to surface 1
Energy Reflected back to surface 2
Energy absorbed by surface 2

## Slide 44
View Factors
Infinite Parallel Gray Planes
Geometric Series

## Slide 45
View Factors
Infinite Parallel Gray Planes

## Slide 46
View Factors – Other Situations
Surface 1
Surface 2
All surfaces are black bodies, n is the total number of surfaces
Enclosure made of black surfaces all at
different temperatures
Two gray bodies exchanging radiation and forming
an enclosure
For parallel large gray surfaces and

## Slide 47
View Factors – Other Situations

## Slide 48
SOME INFORMATION ON THE WEB