## Slide 1
Lecture 8 (Part of Chapter 10)
Objectives
Understand molecular diffusion and how is related to molecular mobility
Define the Fick’s law
Define diffusivity and how it is affected by variables such as pressure, temperature composition, etc.

## Slide 2
Mass Transfer
Fluid Velocity
Assume that molecular species (components) move with the flow of fluid and in addition they are diffusing.
Mass transfer of the components occurs due to the bulk movement of
the fluid (which is somewhat described by fluidmechanics) and due to
diffusion mechanisms.
Molecular Diffusion
Diffusing gases such as
H2 in air
Thomas Graham (1805-1869) during the
period 1828-1833 was investigating diffusion
of gases in other gases.

## Slide 3
Gas | equivalent volume | specific density | Molecular Weight (g/mol)
Hydrogen H2 | 3.83 | 0.0694 | 2
Methane CH4 | 1.344 | 0.455 | 16
Ethylene C2H4 | 1.0191 | 0.972 | 28
Carbon Monoxide CO | 1.0149 | 0.972 | 28
Nitrogen N2 | 1.0143 | 0.972 | 28
Oxygen O2 | 0.9487 | 1.111 | 32
Carbon Dioxide CO2 | 0.812 | 1.527 | 44
Sulfurous Acid SO3H2 | 0.68 | 2.222 | 82
Measured as the change
of volume in the liquid

## Slide 6
The diffusion time is inversely proportional to the
square root of molecular weigh of the diffusing specie

## Slide 7
Graham’s Liquid Diffusion Experiments (Diluted Solutions)
Plate
Diffusion in liquids was several thousands times slower
than in gases
The diffusion process got still slower as the experiment
progressed
Quantities “diffused” are in closed proportion to the quantity of salt in the diffusion solution
Weight percent of sodium chloride | Relative Flux
1 | 1
2 | 1.99
3 | 3.01
4 | 4.00
Experiment Results
water
Salt solution
Salt solution
Water

## Slide 8
Next to Graham’s experiments came Fick’s experiments and models. Fick, born
in 1829, liked very much mathematics but due influences of his brother he became
a Doctor in medicine. In 1847 he was tutored by Carl Ludwig, who strongly believed
that medicine, and indeed life itself, must have a basis in mathematics, physics
and chemistry. In addition to his development to the Diffusion equation, Adolf
Fick’s main discoveries were in physiology, e.g. the area of mechanics
(mechanics applied to the functioning of muscles), hydrodynamics and
hemorheology (viscosity of blood), and in the visual and thermal functioning
of the human body. In 1855 he proposed his famous diffusion equation
mainly based on Graham and his own experimental data
Adolph Fick (1829-1901)

## Slide 9
Fick’s Diffusion Experiments: In a cylindrical tube with a salt reservoir at the
bottom and flowing fresh water at the top
z
Saturated salt solution
and solid salt
Liquid stream of water (component 2) and
salt (component 1) diffusing along the tube
z=L
z=0
Water in the tube (stationary)
Mass of salt diffusing at z
Mass of salt diffusing at
z

## Slide 10
Fick’s Law: From the original paper in 1855
“The diffusion of the dissolved material is
left completely to the influence of the
molecular forces basic to the same law for
the spreading of warmth in a conductor and
which has already been applied with such
great success to the spreading of electricity”
In other words diffusion can be described on the same
mathematical basis as Fourier’s law for heat conduction
or Ohm’s law for electrical conduction

## Slide 11
Electrical Conduction
R
V1
V2
I
Heat Conduction
T1
T2
q
R
1-D Fourier’s Law
Diffusion
R
c1
c2

## Slide 13
Concept on Mass Fluxes (a little more crazy!!!)

## Slide 14
Flux
Area A
Concept on Mass Fluxes
is the vector velocity
and may have three
different directions
ui, vi and wi
In a diffusing mixture the various chemical species (1,2,…..i) are moving
at different velocities ( ). denotes the velocity of the i species
respect to a stationary coordinate system
z
x
y

## Slide 15
Frames of References to study mass transfer
z
x
y
Flux
Area A
Fixed Coordinate System
From a theoretical standpoint the approach is fine, but
practically it may result complicated. We are more
interested in describing how each component of the
mixture (1, 2, …..,i,…n) is moving respect to the bulk

## Slide 16
z
x
y
How could we determine the bulk
velocity of the mixture?
Flux
Area A
Bulk velocity based
on the mass rate
Bulk velocity based
on the moles rate

## Slide 17
Mass Average Velocity
Molar Average Velocity
is the local velocity
that one would measure
by means of a flowmeter

## Slide 18
Flux
Area A
Mass and Molar Average Velocities
Local Rate at which mass passes through a unit
cross section placed perpendicular to the velocity
Local Rate at which moles pass through a unit
cross section placed perpendicular to the velocity

## Slide 19
Diffusion Velocities
Fick’s Law for Diffusion (1D – x direction)
Diffusivity
concentration
gradient

## Slide 20
Fick’s Law for Diffusion
Concentration
Distance from origin
-1
-2
1
2
0
Dt = 0.05
Dt = 0.1
Dt = 0.2
Physical Interpretation of Diffusivity
t = 0
Demonstration

## Slide 21
Physical Interpretation of Diffusivity
Brownian Movement
For N2
0.56 cm in 1 second
zigzag path 475 meters in 1 second
Demonstration 2

## Slide 22
Typical Range of Diffusivities
10-12
10-9
10-8
10-7
10-11
10-10
10-6
10-5
In Solids
In Liquids
In Gases
capillary diffusivity of water
in unsaturated soil
Diffusivity for Gases

## Slide 23
Diffusivity for liquids (non-electrolytes)
r
v
f
Viscosity of
the liquid
Friction
Stokes-Einstein Relation

## Slide 24
Diffusion of gases in porous solids (effective diffusivity)
Transport in cell membrane
  Passive transport (lipid bilayers)
  Active transport
Dispersive Mass Transfer
Dispersion
coefficient
concentration
gradient

## Slide 25
Diffusion in a porous media
Structure of Wood
Transport through cell membrane
Active diffusion
Active transport is the mediated transport
of biochemicals, and other atomic/molecular
substances, across membranes. Unlike passive
transport, this process requires the expenditure of chemical energy to move molecules "uphill" against a gradient.
Membrane Bilayer

## Slide 26
Convective Mass Transfer
Fluid at c2
c1